SAMPLE

PRELIMINARY PLAT CHECKLIST

CITY OF CONSISTENCY PLANNING DEPARTMENT

333 Admin Drive, Consistency, AL 00000

(333) 333-3333/FAX (331) 333-3331

www.xxxxxxxx.xxx

# Name of Plat:

Developer:

Developer’s Engineer/Surveyor:

All  preliminary  plats  submitted  to  the  Planning  Commission  shall  include  with  the application the preliminary plat checklist.  Please check accordingly before submittal.

- Name and address of owners and the designer of the plat. Said designer shall be a land surveyor registered to practice in the State of Alabama.

- Names and addresses of current record (as per the tax assessor’s records) of adjoining property owners, which shall include those across public rights-of-way, other rights-of-way, easements, creeks, etc.

- Date of the plat, north arrow, scale of not less than one inch equals 100 feet, amount of acreage contained in the plat and a statement as to the remaining adjoining acreage the developer or subdivider owns, has an option on or leases.

- Contours shall be shown at an interval of not more than five feet for slopes over five percent, and for slopes less than five percent contours shall be shown at an interval of not more than two feet. All contours shall be based on the true city elevation, which is the USGS-MSL datum. No assumed datum will be accepted. A note on the plat shall indicate which city B.M. was used.

- Lot dimensions, building lines and back and side setback lines and lot and block numbers and proposed street names.

- Rights-of-way, easements, alleys, location and proposed widths.

- Proposed subdivision boundaries, with dimensions and tie to nearest government monument, with description of monument.

- Any pertinent topographic features existing on the site.

- Proposed storm drains, sanitary sewer with approximate sizes and design data.

- Location and dimensions of existing storm and sanitary sewers.

- A statement as to the current and proposed zoning (if applicable); or a statement of the allowable use of each lot.

- A vicinity sketch showing location of proposed site in relation to existing major streets, etc.

- Erosion control measures to be used during construction of the subdivision.

- Width of all proposed paving in the proposed project from back to back of curb.

- Proposed location of “stop,” “yield” and other traffic control signs and devices to be installed. If the proposed subdivision abuts an existing street, the location of any intersecting streets on the other side abutting street shall be depicted.