SAMPLE

SITE PLAN REVIEW CHECK LIST

_______________________________________________ Project

Necessary elements for site plan review applications. Design plans shall include site plans, architectural plans and landscaping plans. A site plan shall be prepared, signed and sealed by an architect, landscape architect, surveyor or an engineer, currently licensed in the State of Alabama, and shall be drawn to a scale of not smaller than 1 inch = 50 feet. Plans shall address the following requirements:

______	a.   Name of development;

______	b.   Location map and north arrow;

______	c.   Dimension, slope and size in square feet of lot; acreage of property;

______	d.   Adjacent properties, streets, service roads, curbs and dimensions of same;

______	e.   Zoning classification of site and of adjacent properties;

______	f.  Existing and proposed buildings, location, size and dimensions;

______	g.   Proposed use of buildings, number of lots and lot numbers if applicable;

______	h.   Number of dwelling units, commercial and density per acre;

______	i.  Lot frontage on public streets and proposed access thereto;

______	j.   Front, side and rear yard (setbacks);

______	k.   Marginal access road and flood plain provisions (as applicable);

______	l.  Off street loading berths or spaces;

______	m.  USGS - MSL - Contours at five-foot intervals;

______	n.   Paved, off street parking, including handicapped parking spaces;

______	o.  Interior/exterior roads, sidewalks, curb and gutters - dimensions and type;

______	p.   Location and specifications of utility lines by type and size. Utility and right-of-way easements;

______	q.   Landscaping  plan  (signed  and  sealed  by  a  registered  landscape  architect).  If  a landscape architect is not available, the applicant may employ a landscape designer;

______	r.   Name and address of owner, development/engineer, architect, landscape architect and contractor (including current license numbers);

______	s.   Location of lighting facilities and on-premise signs;

______	t.  Location of garbage disposal facilities; and

______	u.   Elevations of all faces of buildings and structures, at a scale of  1/8" = 1'0". Such shall indicate:

______	1.   Design character of buildings and structures;

______	2. Specific materials existing/planned for use on buildings and structures, including colors of any and all materials employed, with their locations indicated on the elevations;

______	3.   Heights of buildings and structures;

______	4.   Roofs and overhangs;

______	5.   Special design features, including compliance with American Disabilities Act requirements;

______	6.   Typical locations, shape(s), and type of signs